## Slide 1: Chemin Group-2
Poonam Lakhangaonkar
Hiren Patel
Valentin BERTHOMIER
Rajnish Kumar

## Slide 2: CheMin
CheMin (chemistry and mineralogy) is a mineralogy instrument that identifies and quantifies the minerals present in rocks and soil.
CheMin main modules:
  One 16 dual sample cells sample wheel
  16 piezzo sensors (one per dual cell)
  One X-ray (XRF) for elemental characterization
  One Charge-Coupled Device (CCD)
  Other: inlet cover (sample cell filling), sump (sample cleaming), rotary motors (for turning sample wheel, x-ray calibration), sensors (contamination, position,,,)
It uses a technique called X-ray diffraction, which consists in projecting an X-ray beam on a thin powder sample cell filled by CHIMRA sorting assembly module.
It collects the diffraction pattern on a Charge-Coupled Device (CCD) and creates: - A histogram of number of photon vs photon energy plot, - A one dimensional 2theta plot